## Slide 1: An Agent-Based Model of a Dynamic Mobile Ad-Hoc Network
ECE 508
Wesley Folz

## Slide 2: Agenda
Background
Agent-Based Model
Experiments
Results
Demo
Future Work
Quiz

## Slide 3: Mobile Ad-Hoc Networks
No Infrastructure
  No Centralized Control
Dynamic Topology
  Each can node act as a router
Primarily used in:
  Military Battlefield
  Sensor Networks
  Disaster Areas
  Personal Area Networks
Future uses:
  Internet of Things
  Vehicular Networks
  Etc.
(Bakshi, et. al. 2013)

## Slide 4: Daily Human Mobility Patterns
Human mobility can be characterized by a sequence of visited locations and trips between them (motifs)
Cell phone and survey data
About 90% of people visit less than seven locations per day
  That 90% can be split into 17 different motifs
(Schneider et. al. 2013)

## Slide 5: Agent-Based Model
Three types of Locations:
  Houses
  Workplaces
  Stores (other locations)
Two types of agents:
  workers
  non-workers
Day is split into 48, 30 min time intervals
Each tick represents 1, 30 min time interval

## Slide 6: Human Mobility Model
All Agents:
Agents start the day evenly distributed among the houses
There is a probability that an agent will go ‘out’ (to a store location) during time slot n
If someone went ‘out’ during time slot n they are 10 times more likely to go ‘out’ again during time slot n+1 (
If an agent is at a store during time slot n, they will either travel to a different store or go back to their original location (house or work) during time slot n+1
Agents choose location to travel based on power law distribution ( where r is the distance to a location
(Schneider et. al. 2013)

## Slide 7: Human Mobility Model
Workers:
There is a probability that a worker will go to work during time slot n
The amount of time workers stay it work before going back home is normally distributed: )

## Slide 8: Smart Phone Ad-Hoc Network
Each agent is assumed to have a device (smart phone) connected to the Ad-Hoc Network
Every tick new random sources and destinations are created
Nodes in the network can transmit to other nodes within transmission range
Breadth first search to find route from source to destination with least number of hops
If a node has more routes going through it than the route capacity it dies (gets disconnected from the network)

## Slide 9: Experimentation
Data Gathered
People Moving
  The percentage of people moving during a given time slot
Route Failures
  A route fails if a node in the route dies or moves out of transmission range with its neighbor
Hops Per Route
  The average number of nodes between a source and destination
Destinations Unreachable
  If a route does not exist between the source and destination
Max Routes
  The max number of routes going through a single node
Experiments
Varied number of houses
Varied number of people
  Workers
  Non-workers
Looked at correlations between people movement and:
  Route Failures
  Hops Per Route
  Destinations Unreachable
  Max Routes

## Slide 10: Emergent Results
Chart: Num Houses vs % Route Errors
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
 | 12.7024 | 14.6127 | 11.1533 | 5.9524 | 8.755 | 17.3936 | 18.6313 | 21.3281 | 16.4752 | 16.5704 | 13.8332 | 9.2558 | 17.4157 | 8.3283 | 16.4198 | 19.9817 | 30.0959 | 30.5429 | 21.6629 | 35.3997 | 17.1293 | 31.2404 | 32.6217 | 27.6455 | 20.5034 | 37.0593
Chart: % of People Moving vs % Unreachable
| 0 | 1 | 1.5 | 1 | 0 | 0.5 | 0.5 | 0.5 | 1 | 0 | 0.5 | 0.5 | 3.5 | 3 | 4 | 3 | 7 | 9 | 10.5 | 6.5 | 7 | 6 | 6.5 | 8.5 | 9.5 | 7.5 | 9.5 | 12 | 13 | 10.5 | 9 | 10 | 10 | 13.5 | 16.5 | 12 | 9 | 13 | 12.5 | 12.5 | 9.5 | 10.5 | 9.5 | 10.5 | 8.5 | 8 | 6.5 | 5
 | 0 | 65.3846 | 53.8462 | 69.2308 | 50 | 38.4615 | 61.5385 | 46.1538 | 53.8462 | 65.3846 | 61.5385 | 23.0769 | 50 | 42.3077 | 53.8462 | 11.5385 | 23.0769 | 38.4615 | 7.6923 | 3.8462 | 15.3846 | 7.6923 | 15.3846 | 3.8462 | 0 | 0 | 3.8462 | 11.5385 | 7.6923 | 3.8462 | 0 | 3.8462 | 15.3846 | 23.0769 | 0 | 7.6923 | 7.6923 | 23.0769 | 19.2308 | 0 | 7.6923 | 3.8462 | 0 | 3.8462 | 7.6923 | 0 | 3.8462 | 3.8462
Chart: % People Moving vs % Route Errors

## Slide 11: DEMO

## Slide 12: Future Work
More realistic geography
Increase scale
Run on network simulator to get accurate routing data
  ns3
Use daily mobility model in other applications
  Vehicular networks
  Epidemiology
  Etc.

## Slide 13: Quiz
Generally people travel between less than ___ locations per day.
The distance that people travel between locations follows what type of probability distribution?
True or False: A lot of infrastructure is required to set up a mobile ad-hoc network?
7
Power law (
False

## Slide 14: References
Bakshi A., Sharma A.K., and Mishra A. “Significance of mobile ad-hoc networks (MANETS)” International Journal of Innovative Technology and Exploring Engineering (IJITEE) ISSN: 2278-3075, Volume-2, Issue-4, March 2013
Bhat, C. R. 2001 “Modeling the commute activity-travel pattern of workers: Formulation and empirical analysis.” Transp. Sci. , 35 (1), 61-79
Brockmann, D., Hufnagel, L. and Geisel, T. 2006 “The scaling laws of human travel” Nature 439, 462-465. (DOI 10.1038/nature04292
Hoebeke J., Moerman I., Dhoedt B., and Demeester P. “An overview of mobile ad hoc networks: applications and challenges.” J-Commun Netw 2004;3(3):60–6.
Schneider, C. M., V. Belik, T. Couronne, Z. Smoreda, and M. C. Gonzalez. “Unravelling Daily Human Mobility Motifs.” Journal of The Royal Society Interface 10, no. 84 (April 24, 2013): 20130246–20130246

## Slide 15: Questions?